## Slide 1: Instruction Set Architecture
Instructor Dr. Jianhui Yue
Fall 2015 CSE, Miami Univ.
Notes adapted from MK

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 3: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E

## Slide 4: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 5: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 6: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware

## Slide 7: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 8: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 9: Bit, Byte, Half-word, Word, Double-Word

## Slide 10: Logic View of Memory
By grouping bits together we can store more values
  8 bits = 1 byte
  16 bits = 2 bytes = 1 halfword
  32 bits = 4 bytes = 1 word
From software perspective, memory is an array of bytes, each of which is addressable.
  The byte stored at the memory address 0x20000004 is 10000100
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
0b10000100
0x84
132
Binary
Hexadecimal
Decimal

## Slide 11: Logic View of Memory
When we refer to memory locations by address, we can only do so in units of bytes, halfwords or words
Words
  32 bits = 4 bytes = 1 word
  We have two words:
    0x20000000
    0x20000004
  Can you store a word anywhere? NO.
  A word can only be stored at an address that's divisible by 4.
  Memory address of a word is the lowest address of all four bytes in that word.
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
  Word-address mod 4 = 0

## Slide 12: Logic View of Memory
When we refer to memory locations by address, we can only do so in units of bytes, halfwords or words
Words
  32 bits = 4 bytes = 1 word
  We have two words:
    0x20000000
    0x20000004
  Can you store a word anywhere? NO.
  A word can only be stored at an address that's divisible by 4.
  Memory address of a word is the lowest address of all four bytes in that word.
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
  Word-address mod 4 = 0
Cannot store a word at address 0x20000002.

## Slide 13: Logic View of Memory
When we refer to memory locations by address, we can only do so in units of bytes, halfwords or words
Halfwords
  16 bits = 2 bytes = 1 halfword
  We have four halfwords:
    0x20000000
    0x20000002
    0x20000004
    0x20000006
  Can you store a halfword anywhere? NO.
  A halfword can only be stored at an address that's divisible by 2.
  Memory address of a halfword is the lowest address of its two bytes.
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
  Halfword-address mod 2 = 0

## Slide 14: Logic View of Memory
When we refer to memory locations by address, we can only do so in units of bytes, halfwords or words
Halfwords
  16 bits = 2 bytes = 1 halfword
  We have four halfwords:
    0x20000000
    0x20000002
    0x20000004
    0x20000006
  Can you store a halfword anywhere? NO.
  A halfword can only be stored at an address that's divisible by 2.
  Memory address of a halfword is the lowest address of its two bytes.
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
Cannot store a halfword at address 0x20000001.
  Halfword-address mod 2 = 0

## Slide 15: Question
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
Words
Bytes
Addr.
0003
0002
0001
0000
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
What are the memory address of these four words?
Word 3
Word 2
Word 1
Word 0

## Slide 16: Question (Answer)
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
Words
Bytes
Addr.
0003
0002
0001
0000
Addr
=
0x0012
Addr
=
0x0008
Addr
=
0x0004
Addr
=
0x0000
What are the memory address of these four words?
Word 3
Word 2
Word 1
Word 0

## Slide 17: Endianess
Big Endian: address of most significant byte = word address (xx00 = Big End of word)
Little Endian: address of least significant byte = word address (xx00 = Little End of word)
Intel is Little Endian. MIPS is Big Endian.
msb
lsb
byte 3 byte 2 byte 1 byte 0
Little endian
byte 0 byte 1 byte 2 byte 3
Big endian

## Slide 18: Endianess
Little Endian: address of least significant byte = word address (xx00 = Little End of word)
Big Endian: address of most significant byte = word address (xx00 = Big End of word)
Intell is Little Endian. MIPS is Big Endian.

## Slide 19: Endianess
Little Endian: The little end comes first.
Big Endian: The big end comes first.

## Slide 20: Example
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
0xEE8C90A7
If big endianess is used
The word stored at address 0x20008000 is
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 21: Example
0xA7908CEE
If little endianess is used
The word stored at address 0x20008000 is
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
Endian only specifies byte order, not bit order in a byte!
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 22: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address (Intel processor)

## Slide 23: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 24: Memory Load / Store Instructions
Load a word from memory:
lw Rt, offset(Rs)
Load a byte from memory
lb Rt, offset(Rs)
Store a word to memory
sw Rt, offset(Rs)
Store a byte to memory
sb Rt, offset(Rs)
Compute effective memory address
  [Rs] + offset

## Slide 25: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 26: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 27: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 28: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 29: How store a byte to a 32-bit register?
lb Rt, offset(Rs)
  Rt is a register with 4 bytes
offset(Rs) is byte whose content is 0x12 ?
offset(Rs) is byte whose content is 0x72 ?
1 byte
32-bit Register

## Slide 30: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers

## Slide 31: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 32: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 33: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 34: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 35: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23
§2.5 Representing Instructions in the Computer

## Slide 36: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 37: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 38: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 39: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 40: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations

## Slide 41: Bitwise operations
And &
  1 & 1 = 1; 1 & 0 = 0 ; 0 & 1 = 0; 0 & 0 = 0
Or |
  1 | 1 = 1; 1 | 0 = 1 ; 0 | 1 = 1; 0 | 0 = 0
Not ~
  ~ 1 = 0; ~ 0 =1
Left shift x<<n (Think of x as a bitstring)
  x << n shifts the value of x left by n bits
  4 << 2 = 16
Right shift x>>n (Think of x as a bitstring)
  x >> n shifts the value of x right by n bits
  8 >> 2 = 2

## Slide 42: MIPS Instruction Coding

## Slide 44: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 45: Left Shift Example
4 Bits Left Shift Operation
0000 0000 0000 0000 0000 0000 0000 1001
0000 0000 0000 0000 0000 0000 1001 0000
MIPS instruction
sll $t2, $s0, 4 # reg $t2 = reg $s0 << 4 bits
Machine code
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
0
0
16
10
4
0

## Slide 46: Right Shift Example
4 Bits Right Shift Operation
0000 0000 0000 0000 0000 0000 0001 0000
0000 0000 0000 0000 0000 0000 0000 0001
MIPS instruction
srl $t2, $s0, 4 # reg $t2 = reg $s0 >> 4 bits
Machine code
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
0
0
16
10
4
2

## Slide 47: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 48: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 49: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 50: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 51: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …
Assembler calculates addresses

## Slide 52: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 # i<<2 = i*4 add $t1, $t1, $s6 # t1 = addr. Of save[i] lw $t0, 0($t1) # t0 = save[i] bne $t0, $s5, Exit # go to Exit if cond. false addi $s3, $s3, 1 # i = i+1 j Loop # go to Loop Exit: …

## Slide 53: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 54: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 55: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise

## Slide 56: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 57: Procedure Calls
Basic functionality
  Transfer of parameters & control to procedure
  Transfer of results & control back to the calling program
  Support for nested procedures
What is so hard about this?
  Consider independently compiled code modules
    Where are the inputs?
    Where should I place the outputs?
    Recall: What do you need to know when you write procedures in C?
§2.8 Supporting Procedures in Computer Hardware

## Slide 58: Specifics
Where do we pass data
  Preferably registers  make the common case fast
  Memory as an overflow area
Nested procedures
  The stack, $fp, $sp and $ra
  Saving and restoring machine state
Set of rules that developers/compilers abide by
  Which registers can am I permitted to use with no consequence?
  Caller and callee save conventions for MIPS

## Slide 59: Basic Parameter Passing
Register usage
What about nested calls?
What about excess arguments?
.data
arg1: .word 22, 20, 16, 4
arg2: .word 33,34,45,8
.text
addi $t0, $0, 4
move $t3, $0
move $t1, $0
move $t2, $0
loop: beq $t0, $0, exit
addi $t0, $t0, -1
lw $a0, arg1($t1)
lw $a1, arg2($t2)
jal func
add $t3, $t3, $v0
addi $t1, $t1, 4
addi $t2, $t2, 4
j loop
func: sub $v0, $a0, $a1
jr $ra
exit: ---
$31
$31
PC
PC
+
4
Jal saves the next instruction address, which is return address, to $ra.
Jal restore return address from $ra.

## Slide 60: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 61: MIPS Register Usage Convention

## Slide 62: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j are passed in $a0, …, $a3
  f in $s0 (we need to save $s0 on stack – we will see why later)
  Results are returned in $v0, $v1
$a0
$a1
$a2
$a3
$v0
$v1
argument registers
result registers
procedure

## Slide 63: Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction put in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 64: Stack and Operations
Allows access to only the last item inserted.
An item is inserted or removed from the stack from one end called the “top” of the stack.
This mechanism is called Last-In-First-Out (LIFO).
Push
  the operation to place a new item at the top of the stack
Pop
  the operation to remove the next item from the top of the stack
A
X
R
C
push(M)
A
X
R
C
M
item = pop()
item = M
A
X
R
C

## Slide 65: Stack Implementation
High address
Low address
Stack top
Stack bottom
Stack Pointer(SP)
High address
Low address
Stack top
Stack bottom
High address
Low address
Stack top
Stack bottom
Stack Pointer(SP)
Stack Pointer(SP)
Pop: SP++
Push: SP--

## Slide 66: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 67: Layout of a Stack Frame
Frame pointer ($fp) points to the first word in the currently executing procedure’s stack frame.
The stack pointer ($sp) points to the last word of the frame.

## Slide 68: Procedure Call Mechanics
Old Stack Frame
arg registers
return address
Saved registers
local variables
New Stack
Frame
$fp
$fp
$sp
$sp
Low Address
High Address
compiler
ISA
HW
compiler
addressing
$gp
PC
$sp
stack
dynamic data
static data
text
reserved
System Wide Memory Map

## Slide 69: Example of the Stack Frame
Call Sequence
1. place excess arguments
2. save caller save registers
($a0-$a3, $t0-$t9)
3. jal
4. allocate stack frame
5. save callee save registers
($s0-$s9, $fp, $ra)
6 set frame pointer
Return
1. place function argument in $v0
2. restore callee save registers
3. restore $fp
4. pop frame
5. jr $31
arg 1
arg 2
..
callee
saved
registers
caller
saved
registers
local
variables
..
$fp
$ra
$s0-$s9
$a0-$a3
$t0-$t9
$fp
$sp

## Slide 70: Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
Procedure body
Restore $s0
Result
Return

## Slide 71: Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
Procedure body
Restore $s0
Result
Return
$s0
$s0
$sp
$sp
$sp
High addr.
Low addr.
High addr.
Low addr.
High addr.
Low addr.

## Slide 72: Template for a Procedure
Allocate stack frame (decrement stack pointer)
Save any registers (callee save registers)
Procedure body (remember some arguments may be on the stack!)
Restore registers (callee save registers)
Pop stack frame (increment stack pointer)
Return (jr $ra)

## Slide 73: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 74: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 75
75
Stack frames during the call of fact(7).

## Slide 76: Non-Leaf Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 77: Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call

## Slide 78: Assembly Language and Assemblers
Assembly language is the symbolic representation of a computer’s binary encoding( machine language)
More readable
Assembler translates assembly language to machine codes.
Facilities in Assembler
Macro, assembler directive, label
§Appendix A Assembly Language Programming

## Slide 79: An Example of assembly language program
  .data
  myArray: .word 0:100 # Array of 100 ints initialized all to 0
  .text
  li $t0, 30 # x = 30
  la $t1, myArray # $t1 is base address
  mul $t2, $t0, 4 # $t2 is the offset (4x30)
  add $t3, $t2, $t1 # $t3 = address of myArray[30]
  li $t4, -19 # set $t4 = value to save (-19)
  sw $t4, ($t3) # Store value at address stored in $t3

## Slide 80: Program Structure
Basics
    Simple text file with data declaration, program code (name of file should end with .s or .asm to be used in SPIM or MARS simulator)
    Data declaration section followed by program code section.
Data Declarations
    Placed in section of program identified with assembler directive .data
    Declares variable names used in program; storage allocated in main memory (RAM)
Code
    Placed in section of text identified with assembler directive .text
    Contains program code (instructions)
    Starting point for code (this is not required) is marked by label main:
    Ending point of main code should use exit system call (see System Calls below)

## Slide 81: Program Structure
  The sections of our environment:
  .data
    Allows us to set up “global” variable data that is stored on the computer’s stack.
        myArray: .word -1:10 # create a 10 word array
        msg1: .asciiz “hello” # creates a message for printing on screen
        isMale .byte ‘n’ # creates a byte variable and assigns ‘n’
  .text
    This is where our code begins.
  We can add labels to our source code like this
    main:
    swapLoop:
    Etc…

## Slide 82: Comment
Comments
    Anything following number sign (#) on a line
      # This is a comment… Say anything here…
    Template for a MIPS assembly language program:
        ####################################################################### Author: [Your name goes here]
        # Creation Date: [Date you created this program]
        # Last Modified By and Date: [Who was the last to modify this file and date of modification]
        # Program Name: [name of your program]
        # Objective: [describe what program is designed to do]
        ######################################################################
        .data
        .text
        main:
        exit:
        # End of program. SPIM like it if you leave a blank line

## Slide 83: MIPS Assemble Language Data Types
Data Types
    Instructions are all 32 bits
    byte(8 bits), halfword(2 bytes), word(4 bytes)
    A character requires 1 byte of storage
    An integer requires 1 word (4 bytes) of storage
Literals
    Numbers entered as is (4, 5, etc.)
    Characters enclosed in single quotes (‘a’, ‘b’, ‘c’, etc)
    Strings enclosed in double quotes (“hello world”)

## Slide 84: Declare variables
Format
      name: storage_type value(s)
    Create storage for variable of specified type with given name and specified value
    Value(s) usually gives initial value(s); for storage type .space, gives number of spaces to be allocated
    Note: labels always followed by colon (:)
    Example:
        var1: .word 3 # create a single integer variable with initial value 3
        array1: .byte ‘a’,’b’ # create a 2-element character array with elements initialized to ‘a’ and ‘b’
        array2: .space 40 # allocate 40 consecutive bytes, with storage uninitialized. Could be
        # used as a 40-element character array, or a 10-element integer
        # array; a comment should indicate which it is.

## Slide 85: More MIPS assembler directives
.word w1,…wn Store n words in memory
.byte b1,…, bn, Store the n bytes
.ascii str: Store the string str in memory without null
.asciiz str: Store the string str in memory and null terminate it
.double d1,…,dn, Store the n double floating-point number
.float f1, …, fn, Store the n floating-point number
.data <addr> Subsequent items are stored in data segment
.text<addr> Subsequent items are stored in code segment

## Slide 86: System Call -- syscall
System call is a set of operating system-like services through the syscall instruction
Make system call
  Put the system call code to the register $v0 or $f0
  Put the arguments to register $a0-$a3 or $f0
  Syscall
  Return results are stored in register $v0
You can use syscall to input/output information

## Slide 87: System Call Examples
    Print integer value contained in register $t1
      li $t1, 55 # set $t1 = 55
      li $v0, 1 # load appropriate system call code into register $v0
      # code for printing is 1
      move $a0, $t1 # move integer to be printed into $a0: $a0 = $t1
      syscall # call operating system to perform operation
    Read integer from user and store it in RAM
      li $v0, 5 # load appropriate system call code into register $v0
      # code for reading integers is 5
      syscall # call operating system to perform operation
      sw $v0, int_val # store what user entered into RAM at address int_val
    Print out string (useful for prompts)
      .data
      String1: .asciiz “Print this.” # declaration for string variable
      .text
      main:
      li $v0, 4 # load code for printing strings
      la $a0, string1 # load address of string to be printed into $a0
      syscall # call operating system to perform print operation

## Slide 88
88
Copyright © 2014 Elsevier Inc. All rights reserved.
MIPS System services

## Slide 89: Macros!
The addition of macros was introduced in one of the latest releases of the Mars MIPS Simulator. This was a very useful feature.
A macro file is just like any other assembly file (note: you do not have to have a separate file for this but you should)
Macros have the following format:
.macro macro_name( parameter list )
your code goes here
.end_macro

## Slide 90: Macros!
You can build a macro file and then include this file in your code.
The syntax for including a macro file in your program is:
.include “macro_file_name”
Once you include the file you can call macros just like you call methods
macro_name( parameters )
Lets try one…

## Slide 91: Macro Example-define marco
######################################### Print an Integer
.macro print_int ($x)
li $v0, 1
add $a0, $zero, $x
syscall
.end_macro
######################################### Swap values in registers
.macro swap_int($a, $b)
sw $a, -4($sp)
move $a, $b
lw $b, -4($sp)
.end_macro
##################################### Exit
.macro exit()
li $v0, 10
syscall
.end_macro

## Slide 92: Macro Example – useMacros.asm
.include "macros.asm"
.data
nums: .word 0:20
.text
main:
la $t0, nums # Start address of array
addi $t1, $t0, 80 # End end address of array
li $t2, 10 # Start num to enter into memory
loop:
sw $t2, ($t0) # Store whatever is in $t2 to address stored in $t0
print_int($t2)
newLine()
addi $t2, $t2, 1 # Add one to our variable we will bee saving to memory
addi $t0, $t0, 4 # Update the address of the next element of the array
blt $t0, $t1, loop # loop back up if we have not filled the array
swap:
print_str("\nSwap Numbers...\n")
li $t5, 100
li $t6, 50
print_int($t5)
print_str(", ")
print_int($t6)
print_str("\n=============== Call the swap.\n")
swap_int($t5,$t6)
print_int($t5)
print_str(", ")
print_int($t6)
exit() ########################################## End the program

## Slide 93: Declaring Char Arrays
chrArray: .byte 0:20
    The above allocates 20 bytes of memory and initializes each to 0 (the null character)
    Initialization happens before program execution.
chrArray2: .space 20
    This is an alternative method of allocating 20 bytes of memory.
    No initialization of data so could result in undesired results.
chrArray3: .byte ‘A’, 20
    Allocate 20 bytes (5 words in length) and initialize all to ‘A’
chrArray4: .byte 65, 20
    Same as above but uses the ASCII value of A (65)

## Slide 94: Declaring Int Arrays
  intArray: .word 100:25
    Create 25 words (integer memory chunks) located at word-aligned addresses. Initialize each to 100.
  intArray2: .space 100
    Create 100 bytes (or 25 integer-sized elements) of space

## Slide 95: Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers

## Slide 96: Example: Clearing and Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2

## Slide 97: Comparison of Array vs. Ptr
Multiply “strength reduced” to shift
Array version requires shift to be inside loop
  Part of index calculation for incremented i
  c.f. incrementing pointer
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer

## Slide 98: Using Arrays
  Assembly, as with other languages, can access arrays in a sequential order or in random order. Consider the following C code and the equivalent MIPS version.
  int myArray[100]; // Create an int array of 100 elements
  int x; // Declare x to be the index of element to change
  x = 30 // Set x to the 31th index of array
  myArray[x] = -19 // Set array element[30] to -19
  .data
  myArray: .word 0:100 # Array of 100 ints initialized all to 0
  .text
  li $t0, 30 # x = 30
  la $t1, myArray # $t1 is base address
  mul $t2, $t0, 4 # $t2 is the offset (4x30)
  add $t3, $t2, $t1 # $t3 = address of myArray[30]
  li $t4, -19 # set $t4 = value to save (-19)
  sw $t4, ($t3) # Store value at address stored in $t3

## Slide 99: Using Arrays Example1
  .data
  myArray: .word 0:100 # myArray of 100 integers
  .text
  li $t0, 0 # $t0 is the index, and loop variable
  li $t5, 100 # $t5 is the sentinel value for the loop
  Loop: bge $t0, $t5, Exit_Loop
  la $t1, myArray # $t1 is the base address of myArray
  mul $t2, $t0, 4 # $t2 is the offset
  add $t3, $t2, $t1 # $t3 is the address of desired element
  li $t4, 44 # $t4 is the value 44, to be put in desired element
  sw $t4, ($t3) # save the value of 44 to the array element
  add $t0, $t0, 1 # increment loop variable
  b Loop
  Exit_Loop:
  li $v0, 10
  syscall

## Slide 100: Using Arrays Example 2
  .data
  myArray: .word 0:100 # myArray of 100 integers
  .text
  li $t0, 0 # $t0 is the loop variable
  li $t5, 100 # $t5 is the sentinel value for the loop
  li $t4, 44 # $t4 is the value 44, to be put in desired element
  la $t1, myArray # $t1 starts as the base address of myArray
  # and is the address of each element
  Loop:bge $t0, $t5, Exit_Loop
  sw $t4, ($t1) # Save 44 to the array element at address stored in $t1
  add $t1, $t1, 4 # Add 4 to address to get the next myArray element
  add $t0, $t0, 1 # increment loop induction variable
  b Loop
  Exit_Loop:
  li $v0, 10
  syscall

## Slide 101: Using Arrays Example 3
  .data
  myArray: .word 0:100 # myArray of 100 integers
  .text
  li $t2, 44 # $t2 is the value 44, to be put in desired element
  la $t1, myArray # $t1 starts as the base address of myArray
  # and is the address of each element
  li $t0, 100 # Use $t0 to calculate the address of the last element
  mul $t0, $t0, 4 # Multiple 100 elements by word size (4)
  add $t0, $t0, $t1 # Add address of myArray to 100 x 4 (400)
  # to get last element
  Loop: beq $t1, $t0, Exit_Loop # We check address of $t1
  #(current “pointer”) with last element
  sw $t2, ($t1) # Save 44 to the array element
  # at address stored in $t1
  add $t1, $t1, 4 # Add 4 to address to get the next myArray element
  b Loop
  Exit_Loop:
  li $v0, 10
  syscall

## Slide 102: Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People

## Slide 103: Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword

## Slide 104: String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
  Addresses of x, y in $a0, $a1
  i in $s0

## Slide 105: String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 106: 32-bit Constants
0000 0000 0111 1101 0000 0000 0000 0000
Most constants are small
  16-bit immediate is sufficient
For the occasional 32-bit constant
lui rt, constant
  Copies 16-bit constant to left 16 bits of rt
  Clears right 16 bits of rt to 0
lhi $s0, 61
0000 0000 0111 1101 0000 1001 0000 0000
ori $s0, $s0, 2304
§2.10 MIPS Addressing for 32-Bit Immediates and Addresses

## Slide 107: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
PC-relative addressing
  Target address = PC + offset × 4
  PC already incremented by 4 by this time, which points to the following instruction.

## Slide 108: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 109: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 110: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code
Example
  beq $s0,$s1, L1
  ↓
  bne $s0,$s1, L2 j L1 L2: …
Question1: what is the range of L1?
L1: 16 bits
Question2: what are the range of L1 ?
L1: 26 bits

## Slide 111: Addressing Mode Summary

## Slide 112: Return Address
.data
arg1: .word 22, 20, 16, 4
arg2: .word 33,34,45,8
.text
addi $t0, $0, 4
move $t3, $0
move $t1, $0
move $t2, $0
loop: beq $t0, $0, exit
addi $t0, $t0, -1
lw $a0, arg1($t1)
lw $a1, arg2($t2)
jal func
add $t3, $t3, $v0
addi $t1, $t1, 4
addi $t2, $t2, 4
j loop
func: sub $v0, $a0, $a1
jr $ra
exit: ---
$31
$31
PC
PC
+
4
Jal saves the next instruction address, which is a return address, to $ra.
Jr restores a return address from $ra.

## Slide 113: C Sort Example
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
  void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in $a0, k in $a1, temp in $t0
§2.13 A C Sort Example to Put It All Together

## Slide 114: The Procedure Swap
swap: sll $t1, $a1, 2 # $t1 = k * 4
add $t1, $a0, $t1 # $t1 = v+(k*4)
# (address of v[k])
lw $t0, 0($t1) # $t0 (temp) = v[k]
lw $t2, 4($t1) # $t2 = v[k+1]
sw $t2, 0($t1) # v[k] = $t2 (v[k+1])
sw $t0, 4($t1) # v[k+1] = $t0 (temp)
jr $ra # return to calling routine
1 Allocate registers to program variables
v -> $a0, k ->$a1, temp->$t0
2 Body of procedure
3 Preserve registers across the procedure invocation.
Steps to write a procedure

## Slide 115: The Sort Procedure in C
Non-leaf (calls swap)
  void sort (int v[], int n)
  {
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1;
  j >= 0 && v[j] > v[j + 1];
  j -= 1) {
  swap(v,j);
  }
  }
  }
  v in $a0, k in $a1, i in $s0, j in $s1

## Slide 116: The Procedure Body
move $s2, $a0 # save $a0 into $s2
move $s3, $a1 # save $a1 into $s3
move $s0, $zero # i = 0
for1tst: slt $t0, $s0, $s3 # $t0 = 0 if $s0 ≥ $s3 (i ≥ n)
beq $t0, $zero, exit1 # go to exit1 if $s0 ≥ $s3 (i ≥ n)
addi $s1, $s0, –1 # j = i – 1
for2tst: slti $t0, $s1, 0 # $t0 = 1 if $s1 < 0 (j < 0)
bne $t0, $zero, exit2 # go to exit2 if $s1 < 0 (j < 0)
sll $t1, $s1, 2 # $t1 = j * 4
add $t2, $s2, $t1 # $t2 = v + (j * 4)
lw $t3, 0($t2) # $t3 = v[j]
lw $t4, 4($t2) # $t4 = v[j + 1]
slt $t0, $t4, $t3 # $t0 = 0 if $t4 ≥ $t3
beq $t0, $zero, exit2 # go to exit2 if $t4 ≥ $t3
move $a0, $s2 # 1st param of swap is v (old $a0)
move $a1, $s1 # 2nd param of swap is j
jal swap # call swap procedure
addi $s1, $s1, –1 # j –= 1
j for2tst # jump to test of inner loop
exit2: addi $s0, $s0, 1 # i += 1
j for1tst # jump to test of outer loop
Pass params & call
Move params
Inner loop
Outer loop
Inner loop
Outer loop

## Slide 117: The Full Procedure
sort: addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
… # procedure body
…
exit1: lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine
Save affected registers on stack
Restore affected registers on stack

## Slide 118: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 119
119
Stack frames during the call of fact(7).

## Slide 120: Non-Leaf Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 121: Translation and Startup
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 122: Assembler Pseudoinstructions
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: figments of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary

## Slide 123: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: described contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 124: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 125: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including $sp, $fp, $gp)
  6. Jump to startup routine
    Copies arguments to $a0, … and calls main
    When main returns, do exit syscall

## Slide 126: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions

## Slide 127: Effect of Compiler Optimization
Compiled with gcc for Pentium 4 under Linux

## Slide 128: Effect of Language and Algorithm

## Slide 129: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 130: ARM & MIPS Similarities
ARM: the most popular embedded core
Similar basic set of instructions to MIPS
§2.16 Real Stuff: ARM Instructions
 | ARM | MIPS
Date announced | 1985 | 1985
Instruction size | 32 bits | 32 bits
Address space | 32-bit flat | 32-bit flat
Data alignment | Aligned | Aligned
Data addressing modes | 9 | 3
Registers | 15 × 32-bit | 31 × 32-bit
Input/output | Memory mapped | Memory mapped

## Slide 131: Compare and Branch in ARM
Uses condition codes for result of an arithmetic/logical instruction
  Negative, zero, carry, overflow
  Compare instructions to set condition codes without keeping the result
Each instruction can be conditional
  Top 4 bits of instruction word: condition value
  Can avoid branches over single instructions

## Slide 132: Instruction Encoding

## Slide 133: Basic x86 Registers
§2.17 Real Stuff: x86 Instructions

## Slide 134: Basic x86 Addressing Modes
Two operands per instruction
Source/dest operand | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate
Memory addressing modes
  Address in register
  Address = Rbase + displacement
  Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
  Address = Rbase + 2scale × Rindex + displacement

## Slide 135: x86 Instruction Encoding
Variable length encoding
  Postfix bytes specify addressing mode
  Prefix bytes modify operation
    Operand length, repetition, locking, …

## Slide 136: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Make the common case fast
  4. Good design demands good compromises
Layers of software/hardware
  Compiler, assembler, hardware
MIPS: typical of RISC ISAs
  c.f. x86
§2.20 Concluding Remarks

## Slide 137: Concluding Remarks
Measure MIPS instruction executions in benchmark programs
  Consider making the common case fast
  Consider compromises
Instruction class | MIPS examples | SPEC2006 Int | SPEC2006 FP
Arithmetic | add, sub, addi | 16% | 48%
Data transfer | lw, sw, lb, lbu, lh, lhu, sb, lui | 35% | 36%
Logical | and, or, nor, andi, ori, sll, srl | 12% | 4%
Cond. Branch | beq, bne, slt, slti, sltiu | 34% | 8%
Jump | j, jr, jal | 2% | 0%