## Slide 1: Logic Gates and Combinational Logic Circuits
Instructor Dr. Jianhui Yue
Fall 2015 CSE, Miami Univ.
Notes adapted from Hakim Weatherspoon
See: Textbook Appendix B.2 and B.3 (Also, see B.1)

## Slide 2: Outline
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 3: A switch
Acts as a conductor or insulator
Can be used to build amazing things…
The Bombe used to break the German
Enigma machine during World War II
Notes: Pictures show the Bombe built by Alan Turing to break the enigma machine ciphers.
They were Fixed-Program Computers came before stored-program computers (general purpose)
The former required re-wiring (e.g. ENIAC took 3 weeks to “re-wire”).

## Slide 4: Basic Building Blocks: Switches to Logic Gates
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
+
-
A
B
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
Truth Table
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 5: Basic Building Blocks: Switches to Logic Gates
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
A | B | Light
+
-
-
A
B
A
B
A | B | Light
OFF | OFF | OFF
OFF | ON | ON
ON | OFF | ON
 |  | ON
Truth Table
+
Notes: Speed and size of a mechanical switch

## Slide 6: Basic Building Blocks: Switches to Logic Gates
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
A | B | Light
+
-
-
A
B
A
B
A | B | Light
OFF | OFF | OFF
OFF | ON | ON
ON | OFF | ON
 |  | ON
Truth Table
+
Notes: Speed and size of a mechanical switch

## Slide 7: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
+
-
-
A | B | Light
OFF | OFF | OFF
OFF | ON | ON
ON | OFF | ON
ON | ON | ON
A
B
A
B
A | B | Light
OFF | OFF | OFF
OFF | ON | OFF
ON | OFF | OFF
ON | ON | ON
Truth Table
+
Notes: Speed and size of a mechanical switch

## Slide 8: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
-
-
A
B
A
B
A | B | Light
OFF | OFF | OFF
OFF | ON | ON
ON | OFF | ON
ON | ON | ON
A | B | Light
OFF | OFF | OFF
OFF | ON | OFF
ON | OFF | OFF
ON | ON | ON
Truth Table
OR
AND
Notes: Speed and size of a mechanical switch

## Slide 9: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
-
-
A
B
A
B
A | B | Light
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Light
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
0 = OFF
1 = ON
OR
AND
Notes: Speed and size of a mechanical switch

## Slide 10: Basic Building Blocks: Switches to Logic Gates
Did you know?
George Boole Inventor of the idea of logic gates. He was born in Lincoln, England and he was the son of a shoemaker in a low class family.
A
B
A
B
George Boole,(1815-1864)
OR
AND
Notes: E.g. logic statements:
“Jane will only go to the cinema tonight if a good film is on AND she has enough money.”
“Stuart will only go to the birthday party on Sunday if Katie OR Sujit is going too.”

## Slide 11: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 12: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
Notes: Flash Drives
Create truth table of AND or OR: state what they do

## Slide 13: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
Notes: Flash Drives
Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 14: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
Notes: Flash Drives
Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 15: Activity#1: Logic Gates
Fill in the truth table, given the following Logic Circuit made from Logic AND, OR, and NOT gates.
What does the logic circuit do?
a
b
Out
a | b | Out
Notes: Fill out table
Put, NOT, AND, OR labels in box

## Slide 16: Activity#1: Logic Gates
XOR: out = 1 if a or b is 1, but not both;
out = 0 otherwise.
out = 1, only if a = 1 AND b = 0
OR a = 0 AND b = 1
a | b | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a
b
Out
Notes: Fill out table

## Slide 17: Activity#1: Logic Gates
XOR: out = 1 if a or b is 1, but not both;
out = 0 otherwise.
out = 1, only if a = 1 AND b = 0
OR a = 0 AND b = 1
a | b | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a
b
Out
Notes: Fill out table
Remove instructions

## Slide 18: Activity#2: Logic Gates
Fill in the truth table, given the following Logic Circuit made from Logic AND, OR, and NOT gates.
What does the logic circuit do?
a
b
d
Out
a | b | d | Out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: Fill out table

## Slide 19: Activity#2: Logic Gates
Multiplexor: select (d) between two inputs (a and b) and set one as the output (out)?
out = a, if d = 0
out = b, if d = 1
a | b | d | Out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a
b
d
Out
Notes: Fill out table
Ask rows in audience to fill in different rows of tabel

## Slide 20: Outline
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 21: Next Goal
Given a Logic function, create a Logic Circuit that implements the Logic Function…
…and, with the minimum number of logic gates
Fewer gates: A cheaper ($$$) circuit!
Notes: Can get logic circuit from truth table
Minimize logic circuit through algebraic reductions or Karnaugh Maps

## Slide 22: Logic Gates
NOT:
AND:
OR:
XOR:
  .
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 23: Logic Gates
NOT:
AND:
OR:
XOR:
  .
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
XNOR:
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 24: Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 25: Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
NAND:
  out = = !(a & b) =  (a  b)
NOR:
  out = = !(a | b) =  (a  b)
XNOR:
  out = = ab +
  .
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 26: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a ∙ 0 =
  a ∙ 1 =
  a ∙ ā =
Notes: Minimization activity
Maybe use picture to go through
Complement a+ā=1 and aā=0

## Slide 27: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a ∙ 0 =
  a ∙ 1 =
  a ∙ ā =
  a
  1
  1
  0
  a
  0
a
b
a
b
Notes: Minimization activity
Maybe use picture to go through
Complement a+ā=1 and aā=0

## Slide 28: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  =
  =
  a + a b =
  a(b+c) =
  =
Notes: Minimization activity
Maybe use picture to go through
  De Morgan’s Law: = ∙ and = +
Minimization activity
Maybe use picture to go through
  De Morgan’s Law: ((a+b)) ̅ = a ̅ ∙ b ̅ and ((a ∙b)) ̅ = a ̅ + b ̅

## Slide 29: De Morgan’s Law
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
x | y | z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 30: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  =
  =
  a + a b =
  a(b+c) =
  =
  ∙
  +
  a
  ab + ac
  + ∙
A
B
A
B
↔
A
B
A
B
↔
Notes: Minimization activity
Maybe use picture to go through
  De Morgan’s Law: = ∙ and = +
Minimization activity
Maybe use picture to go through
  De Morgan’s Law: ((a+b)) ̅ = a ̅ ∙ b ̅ and ((a ∙b)) ̅ = a ̅ + b ̅

## Slide 31: Activity #3: Identities
a + 0 =
a + 1 =
a + ā =
a 0 =
a 1 =
a ā =
=
=
a + a b =
a(b+c) =
=
  a
  1
  1
  0
  a
  0
  +
  a
  ab + ac
  + ∙
Show that the Logic equations
below are equivalent.
(a+b)(a+c) = a + bc
(a+b)(a+c) =
Notes: Minimization activity

## Slide 32: Activity #3: Identities
a + 0 =
a + 1 =
a + ā =
a 0 =
a 1 =
a ā =
=
=
a + a b =
a(b+c) =
=
  a
  1
  1
  0
  a
  0
  +
  a
  ab + ac
  +
Show that the Logic equations
below are equivalent.
(a+b)(a+c) = a + bc
(a+b)(a+c) = aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc
Notes: Minimization activity

## Slide 33: Logic Manipulation
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 34: Logic Manipulation
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
 |  |  |  |  |  | bc | RHS
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 1 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 1 | 1
 |  |  | a+b | a+c | LHS |  | 
 |  |  | 0 | 0 | 0 |  | 
 |  |  | 0 | 1 | 0 |  | 
 |  |  | 1 | 0 | 0 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 35: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 36: Outline
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 37: Next Goal
How to standardize minimizing logic circuits?

## Slide 38: Logic Minimization
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: Draw circuit and go through out=true cases
Have not done cheaply yet

## Slide 39: Logic Minimization
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Write minterms
sum of products:
OR of all minterms where out=1
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c
Notes: Show what out equals

## Slide 40: Logic Minimization
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Write minterms
sum of products:
OR of all minterms where out=1
  E.g. out = c + bc + ac
corollary: any combinational circuit can be implemented in two levels of logic (ignoring inverters)
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c
c
out
b
a
Notes: Show what out equals

## Slide 41: Karnaugh Maps
        How does one find the most efficient equation?
          Manipulate algebraically until…?
          Use Karnaugh maps (optimize visually)
          Use a software optimizer
          For large circuits
          Decomposition & reuse of building blocks

## Slide 42: Minimization with Karnaugh maps (1)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac

## Slide 43: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Karnaugh maps identify which inputs are (ir)relevant to the output
The rows and columns of map represent different combinations of inputs.
Each cell is the logic function output under its corresponding inputs.
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab
The ordering of col.s/rows : the col.s/rows are numbered so that the binary representations for the numbers of two adjacent col.s/rows differ in exactly one position.

## Slide 44: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Karnaugh maps identify which inputs are (ir)relevant to the output
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 45: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Karnaugh map minimization
  Cover all 1’s
  Group adjacent blocks of 2n 1’s that yield a rectangular shape
  Encode the common features of the rectangle
    out = a + c
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 46: Karnaugh Minimization Tricks (1)
Minterms can overlap
  out = b + a + ab
Minterms can span 2, 4, 8 or more cells
  out = + ab
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 47: Karnaugh Minimization Tricks (1)
Minterms can overlap
  out = b + a + ab
Minterms can span 2, 4, 8 or more cells
  out = + ab
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 48: Karnaugh Minimization Tricks (2)
The map wraps around
  out = d
  out =
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 49: Karnaugh Minimization Tricks (2)
The map wraps around
  out = d
  out =
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 50: Karnaugh Minimization Tricks (3)
“Don’t care” values can be interpreted individually in whatever way is convenient
  assume all x’s = 1
  out = d
  assume middle x’s = 0
  assume 4th column x = 1
  out =
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 51: Karnaugh Minimization Tricks (3)
“Don’t care” values can be interpreted individually in whatever way is convenient
  assume all x’s = 1
  out = d
  assume middle x’s = 0
  assume 4th column x = 1
  out =
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 52: Karnaugh Map Group Rules
  All groups in the entire grid must be made up with all 1’s.
  Groups can not be made diagonally.
  Groups can only be made as a power of 2 (20, 21, 22, 23, …) ie (1,2,4,8,…)
  Groups should be as large as possible
  All 1’s on the grid must be grouped
  You are allowed to overlap groups and always attempt to do so
  You are allowed to wrap around the grid

## Slide 53: Multiplexer
A multiplexer selects between multiple inputs
  out = a, if d = 0
  out = b, if d = 1
Build truth table
Minimize diagram
Derive logic diagram
a
b
d
a | b | d | out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: What is the truth table

## Slide 54: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build a truth table
  out = bd + a + ab + abd
a
b
d

## Slide 55: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build the Karnaugh map
00 01 11 10
0
1
d
ab
a
b
d

## Slide 56: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build the Karnaugh map
0 | 0 | 1 | 1
0 | 1 | 1 | 0
00 01 11 10
0
1
d
ab
a
b
d

## Slide 57: Multiplexer Implementation
Derive Minimal Logic Equation
  out = a + bd
d
out
b
a
00 01 11 10
0
1
d
ab
0 | 0 | 1 | 1
0 | 1 | 1 | 0
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a
b
d

## Slide 58: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.
Any logic function can be implemented as “sum of products”. Karnaugh Maps minimize number of gates.
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 59: Outline
From Transistors to Gates to Logic Circuits
Logic Gates
  From transistors
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Desing Adder

## Slide 60: Binary Addition
Binary addition requires
  Add of two bits PLUS carry-in
  Also, carry-out if necessary
Notes: Talk about Cin (carry in) and Cout (carry out)
Animate this better
Add another slide
So we need two numbers, the sum, carry in, and carry out

## Slide 61: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
A
B
S
Cout
A | B | Cout | S
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 62: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
S = B + A
Cout = AB
A
S
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Cout
S
A
B
A
B
S
Cout
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 63: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
S = B + A = A  B
Cout = AB
A
S
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Cout
S
A
B
A
B
S
Cout
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 64: 1-bit Adder with Carry
A | B | Cin | Cout | S
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
Activity: Truth Table and Sum-of-Product.
Logic minimization via Karnaugh Maps and algebraic minimization.
Draw Logic Circuits
A
B
Cout
S
Cin

## Slide 65: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
Cout = BC + AC + AB + ABC
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
A
B
Cout
S
Cin
Cout
S
A
B
Cin
B
Notes: Draw circuits

## Slide 66: 1-bit Adder with Carry
A
B
S
Ci
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
Cout = BC + AC + AB + ABC
00 01 11 10
0
1
Cin
AB
00 01 11 10
0
1
Cin
AB
Cout
S
S
Cout
S
A
B
Cin
B
A
B
Cout
S
Cin

## Slide 67: 1-bit Adder with Carry
A
B
S
Ci
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
Cout = BC + AC + AB + ABC
Cout = AB + AC + BC
0 | 0 | 1 | 0
0 | 1 | 1 | 1
00 01 11 10
0
1
Cin
AB
0 | 1 | 0 | 1
1 | 0 | 1 | 0
00 01 11 10
0
1
Cin
AB
Cout
S
S
Cout
S
A
B
Cin
B
A
B
Cout
S
Cin

## Slide 68: 1-bit Adder with Carry
S
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
S = (C + B) + A( + BC)
S = (B  C) + A()
S = A  (B  C)
Cout = BC + AC + AB + ABC
Cout = AB + AC + BC
0 | 0 | 1 | 0
0 | 1 | 1 | 1
00 01 11 10
0
1
Cin
AB
0 | 1 | 0 | 1
1 | 0 | 1 | 0
00 01 11 10
0
1
Cin
AB
Cout
S
A
B
Cout
S
Cin
S
A
B
Cin
Cout

## Slide 69: 1-bit Adder with Carry
S
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
S = (C + B) + A( + BC)
S = (B  C) + A()
S = A  (B  C)
Cout = BC + AC + AB + ABC
Cout = BC + AC + AB( + C)
Cout = BC + AC + AB
Cout = (B + A)C + AB
Cout = (A  B)C + AB
A
B
Cout
S
Cin
S
A
B
Cin
Cout

## Slide 70: 1-bit Adder with Carry
S
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
S = (C + B) + A( + BC)
S = (B  C) + A()
S = A  (B  C)
Cout = BC + AC + AB + ABC
Cout = BC + AC + AB( + C)
Cout = BC + AC + AB
Cout = (B + A)C + AB
Cout = (A  B)C + AB
A
B
Cout
S
Cin

## Slide 71: 4-bit Adder (Assignment)
4-Bit Full Adder
Adds two 4-bit numbers and carry in
Computes 4-bit result and carry out
Can be cascaded
Cout
A[4]
B[4]
S[4]
Cin
Notes: Adds two 1-bit numbers, along with carry-in, computes 1-bit result and carry out
Can be cascaded to add N-bit numbers

## Slide 72: 4-bit Adder (Assignment)
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
Carry-out = overflow indicates result does not fit in 4 bits

## Slide 73: Binary Subtraction
Two’s Complement Subtraction
  Subtraction is simply addition,
  where one of the operands has been negated
    Negation is done by inverting all bits and adding one
    A – B = A + (-B) = A + ( + 1)
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 74: Activity#4 How do we build electronic switches?
Transistors:
6:10 minutes (watch from from 41s to 7:00)
http://www.youtube.com/watch?v=QO5FgM7MLGg
Fill our Transistor Worksheet with info from Video
Notes: Everything that we have shown them can be constructed in silicon.

## Slide 75: NMOS and PMOS Transistors
NMOS Transistor
Connect source to drain when gate = 1
N-channel
VD
VS = 0 V
VG
VG = VS
VG = 0 V
PMOS Transistor
Connect source to drain when gate = 0
P-channel
VS= 0 V
VD
VG
VG = VS
VG = 0 V

## Slide 76: NMOS and PMOS Transistors
NMOS Transistor
Connect source to drain when gate = 1
N-channel
VD
VS = 0 V
VG
VG = 1
VG = 0
PMOS Transistor
Connect source to drain when gate = 0
P-channel
VG
VG = 1
VG = 0
VS= 0 V
VD

## Slide 77: Inverter

## Slide 78: Inverter

## Slide 79: NAND Gate

## Slide 80: NOR Gate

## Slide 81: Logic Gates
One can buy gates separately
  ex. 74xxx series of integrated circuits
  cost ~$1 per chip, mostly for packaging and testing
Cumbersome, but possible to build devices using gates put together manually

## Slide 82: Then and Now
The first transistor
  on a workbench at
  AT&T Bell Labs in 1947
  Bardeen, Brattain, and Shockley
An Intel Haswell
  1.4 billion transistors
  177 square millimeters
  Four processing cores
http://techguru3d.com/4th-gen-intel-haswell-processors-architecture-and-lineup/
Notes: John Bardeen
Walter Brattain
William Shockley

## Slide 83: Then and Now
The first transistor
  on a workbench at
  AT&T Bell Labs in 1947
  Bardeen, Brattain, and Shockley
An Intel Westmere
  1.17 billion transistors
  240 square millimeters
  Six processing cores
http://www.theregister.co.uk/2010/02/03/intel_westmere_ep_preview/
Notes: John Bardeen
Walter Brattain
William Shockley

## Slide 84: Summary
Most modern devices are made from billions of on /off switches called transistors
  We will build a processor in this course!
  Transistors made from semiconductor materials:
    MOSFET – Metal Oxide Semiconductor Field Effect Transistor
    NMOS, PMOS – Negative MOS and Positive MOS
    CMOS – complementary MOS made from PMOS and NMOS transistors
  Transistors used to make logic gates and logic circuits
We can now implement any logic circuit
  Can do it efficiently, using Karnaugh maps to find the minimal terms required
  Can use either NAND or NOR gates to implement the logic circuit
  Can use P- and N-transistors to implement NAND or NOR gates