## Slide 1: Sequential Logic Circuits
Instructor Dr. Jianhui Yue
See P&H Appendix B.7. B.8, B.10, B.11
Adopted notes from Hakim Weatherspoon

## Slide 2: Hint1 for Project 1
1 Hash Table instructionTypeTable
Hashtable<String, Integer> instructionTypeTable
= new Hashtable<String, Integer>();
instructionTypeTable.put(“lw", 2);
instructionTypeTable.put(“sw", 2);
instructionTypeTable.put(“add", 1);
2 To retrieve an instruction type
Integer InstFmt = instructionTypeTable.get(“lw");

## Slide 3: Hint2 for Project 1
Framework
inst = getInst( line );
instType = instructionTypeTable.get(inst) ;
switch( instType )
{
case 1: // R-format
do_R_foramat( line );
break;
case 2: // I-format
do_I_foramat( line );
break;
case 3: // J-format
do_J_format( line );
break;
default :
report_error( line );
}

## Slide 4: Hint3 for Project 1
Do_R_format( string line )
{
Scanner s = new Scanner( line );
string inst = s.next();
if( inst != “sll” ){
rs = s.next( );
s.next();
rt = s.next();
s.next();
rd = s.next( );
encoding_R_Inst( inst, rs, rt, rd);
}else{
…
encoding_R_Inst_shamt( inst, rs, rt, rd, shamt);
}
…
}
add $1 , $2 , $3

## Slide 5: Big Picture: Building a Processor
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 6: Review
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
A0 B0
S0
A1 B1
S1
A2 B2
S2
A3 B3
S3
C0
1-bit adder

## Slide 7: Review
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
S0
S1
S2
S3
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub

## Slide 8: Example: A Calculator
decoder
8
8
S
A
B
8
0=add
1=sub
Notes: red herring? constants into mux

## Slide 9: Example: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
Notes: red herring? constants into mux

## Slide 10: Example: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
128
128
0b1000 0000
0b1000 0000
Notes: red herring? constants into mux

## Slide 11: Example: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
128
128
0b1000 0000
0b1000 0000
Notes: red herring? constants into mux

## Slide 12: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
S0
S1
S2
S3
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub

## Slide 13: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
  Assume each 1-bit full adder delay is 2 ns

## Slide 14: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
S0
S1
S2
S3
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub
t=8
t=6
t=4
t=2
t=0

## Slide 15: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
  Can we store the result?
S0
S1
S2
S3
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub
t=8
t=6
t=4
t=2
t=0

## Slide 16: Performance
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
Combinational
Logic
tcombinational
inputs arrive
outputs expected

## Slide 17: 4-bit Ripple Carry Adder
A3
B3
S3
C4
A1
B1
S1
A2
B2
S2
A0
B0
C0
S0
C1
C2
C3
First full adder, 2 ns delay
Second full adder, 2 ns delay
…
Carry ripples from lsb to msb
Notes: Carry-lookahead adders would be more efficient performance wise (i.e. lower gate delay), but more expense hardware wise (i.e. more logic gates)

## Slide 18: Motivations for Stateful Components
Until now is combinationial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 19: Goals
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 20: Goal
How do we store store one bit?

## Slide 21: First Attempt: Unstable Devices
B
A
C

## Slide 22: First Attempt: Unstable Devices
Does not work!
  Unstable
  Oscillates wildly!
A
B
0
1
C
1
0
0
1
A
B
0
0
C
1
1
0
1
A = 1  B = 0  C = 1
C = 1  A = 0  B = 1

## Slide 23: Second Attempt: Bistable Devices
In stable state, A = B
How do we change the state?
A
B
A
B
1
A
B
1
0
0
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 24: Third Attempt: Set-Reset Latch
B
R
Q
A
S
Notes: Can you store a value (with this circuit)?
Can you change its value?
Q is comes from Latin language "quiscens" or "the present particle" or "what is present available" or "present output"
How to create state? Feedback.
Show how the signal works

## Slide 25: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Either of inputs is 1, NOR is 0

## Slide 26: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
Q = (R+Q) = RQ
If R = 1, Q = 0
If Q= 0 and S = 0, Q = 1
S | R | Q | 
0 | 0 |  | 
0 | 1 | ? | ?
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | ? | ?
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0
1
0
Q will be 0 if R is 1
1
will be 1
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 |  | 
1 | 1 |  | 

## Slide 27: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | ? | ?
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | ? | ?
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
1
0
1
Q will be 1
0
will be 0 if S is 1
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
What are the values for Q and ?
0 and 0
0 and 1
1 and 0
1 and 1

## Slide 28: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
Q = (R+Q) = RQ = Q (if R = 0)
Q = (S+Q) = SQ = Q (if S = 0)
S | R | Q | 
0 | 0 | ? | ?
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 | ? | ?
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0
0
1
If Q is 1, will stay 1
if Q is 0, will stay 0
0
If is 0 will stay 0
If is 1 will stay 1
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
1

Notes: Since the set and reset input are both 0, the Q and !Q determine the output, which will hold.

## Slide 29: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
1
1
0
Q will be 0 since R is 1
0
will be 0 since S is 1
What happens when S,R changes from 1,1 to 0,0?
Either of inputs is 1, NOR is 0
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 30: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
10
1 0
01
0 1
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
What happens when S,R changes from 1,1 to 0,0?
Q and become unstable and will oscillate wildly
between values 0,0 to 1,1 to 0,0 to 1,1 …
0 1 0
01 0
0 1 0 1
01 0 1
0
0
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 31: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S
R
Q
S
R
Q
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 32: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.

## Slide 33: Next Goal
How do we avoid the forbidden state of S-R Latch?

## Slide 34: Fourth Attempt: (Unclocked) D Latch
Fill in the truth table?
D
S
R
Q
Q
D
D | Q | 
0 |  | 
1 |  | 
D | Q | 
0 |  | 
1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 35: Fourth Attempt: (Unclocked) D Latch
D
S
R
Q
Q
D
D | Q | 
0 | 0 | 1
1 | 1 | 0
D | Q | 
0 | 0 | 1
1 | 1 | 0
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Fill in the truth table?
Data (D) Latch
  Easier to use than an SR latch
  No possibility of entering an undefined state
When D changes, Q changes
    … immediately (…after a delay of 2 Ors and 2 NOTs)
Need to control when the output changes
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 36: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding the forbidden state.

## Slide 37: Next Goal
How do we coordinate state changes to a D Latch?

## Slide 38: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period; frequency = 1/period
period
high
low
1
0
falling edge
rising edge
clock
period
clock
high
clock
low
rising edge
falling edge

## Slide 39: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 40: Clock Methodology
Clock Methodology
Negative edge, synchronous
    Edge-Triggered: Signals must be stable near falling clock edge
Positive edge synchronous
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 41: Fifth Attempt: D Latch with Clock
S
R
D
Q
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 42: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Fill in the truth table
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 43: Fifth Attempt: D Latch with Clock
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
D
clk
Q
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Fill in the truth table
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 44: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 45: Sixth Attempt: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
L
L
clk
D
X
Q
c
X
c
Q
D
clk
0
0
1
0
1
Activity#1: Fill in timing graph and values for X and Q
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 46: Sixth Attempt: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
L
L
clk
D
X
Q
c
X
c
Q
D
clk
1
0
1
0
0
1
1
0
0
1
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 47: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flop (aka Master-Slave D Flip-Flop) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.

## Slide 48: Next Goal
How do we store more than one bit, N bits?

## Slide 49: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk

## Slide 50: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.
An N-bit register stores N-bits. It is created with N D-Flip-Flops in parallel along with a shared clock.

## Slide 51: An Example: What will this circuit do?
4-bit
reg
Clk
Decoder
+1
4
4
4
16
4

## Slide 52: An Example: What will this circuit do?
4-bit
reg
Clk
Run
WE
R
Reset
Decoder
A[4]
1 = 0001 =B[4]
S[4]
Cout
+1
4
4
4
16
4

## Slide 53: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0
Notes: Previous slide would need to display up to 16, so would need a 16-segment LED decoder

## Slide 54: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0

## Slide 55: Decoder Example: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 56: 7 Segment LED Decoder Implementation
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 57: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 58: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 59: Encoders
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Log2(N) outputs wires
N Input wires
e.g. Voting:
Can only vote for one out of N
candidates, so N inputs.
But can encode vote efficiently
with binary encoding.
Notes: N possible inputs -> log2(N) wires to encode

## Slide 60: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  |  |  | 
0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
o0
o1
o2
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 61: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  | o2 | o1 | o0
0 | 0 | 0 | 0 |  | 0 | 0 | 0
1 | 0 | 0 | 0 |  | 0 | 0 | 1
0 | 1 | 0 | 0 |  | 0 | 1 | 0
0 | 0 | 1 | 0 |  | 0 | 1 | 1
0 | 0 | 0 | 1 |  | 1 | 0 | 0
o0
o1
o2
o2 = abcd
o1 = abcd + abcd
o0 = abcd + abcd
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 62: Basic Building Blocks Example: Voting
Ballots
The 3410 optical scan
vote reader
machine
detect
enc
8
3
7
7LED decode

## Slide 63: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 64: Recap
We can now build interesting devices with sensors
  Using combinationial logic
We can also store data values (aka Sequential Logic)
  In state-holding elements
  Coupled with clocks

## Slide 65: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 66: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 67: Finite State Machines

## Slide 68: Next Goal
How do we design logic circuits with state?

## Slide 69: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 70: Abstract Model of FSM
Machine is
M = ( S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 71: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic Clock edge triggers the state transitions
Next State
Current State
Input
Output
Registers
Comb. Logic
Clock
Notes: Put sequential logic term on slide

## Slide 72: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 73: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: = up or = down
Output: = on or = off
States: = A, = B, = C, or = D
Notes: Say left of slash is input and right is output

## Slide 74: FSM Example
Legend
S1S0
i0i1i2…/o0o1o2…
S1S0
00
01
10
11
1/1
0/0
1/1
1/0
0/0
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 0=off
States: 00=A, 01=B, 10=C, or 11=D

## Slide 75: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic
Clock

## Slide 76: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic
Clock

## Slide 77: Moore Machine FSM Example
Legend
state out
input
startout
A off
B on
C off
D off
down
up
down
down
up
up
down
up
Input: up or down
Output: on or off
States: A, B, C, or D
Notes: Also show a mealy machine

## Slide 78: Mealy Machine FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 79: Example 1
Draw a state transition diagram for a decimal counter which counts from 0~9 and carry 1 when meeting 10(decimal)

## Slide 80: Analysis
There is no input : when power on, it will count automatically.
Output : when meeting 10(decimal), the output is 1.
Binary code assignment
Q3Q2Q1Q0 ( but actual state is from 0~9)
0000
0001
0010
0011
0100
1001
1000
0111
0110
0101
/0
/0
/0
/0
/0
/0
/0
/0
/0
/1

## Slide 81: Example 2
A vending machine selling a 20 cent item
Input could be 5 , 10 cents
– Input
– Output
– State ?
cents already in the machine

## Slide 82: State Machine
States
00 – 0 cents, 01 – 5cents, 10 – 10cents, 11 – 15cents
Input x
‘0’ – 5 cents ‘1’, – 10 cents
Output : ‘0’ - no item, ‘1’ – dispense item
00
01
10
11
1/0
1/1
0/0
0/0
1/0
1/1
0/1
0/0

## Slide 83: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Notes: Ask as a clicker question

## Slide 84: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Carry-out
1
Notes: Ask as a clicker question

## Slide 85: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Carry-in
1
Notes: Ask as a clicker question

## Slide 86: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Carry-out
1
1
Sum: output
Notes: Ask as a clicker question

## Slide 87: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
  How many states are needed to represent FSM?
  Draw and Fill in FSM diagram
…10110
…01111
…00101
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Sum: output
Notes: Ask as a clicker question

## Slide 88: FSM: State Diagram
states:
Inputs: ??? and ???
Output: ???
  .
…10110
…01111
…00101
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 89: FSM: State Diagram
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  .
…10110
…01111
…00101
a
b
z

## Slide 90: FSM: State Diagram
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  Arcs labeled with input bits a and b, and output z
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
…10110
…01111
…00101
a
b
z
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 91: FSM: State Diagram
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  Arcs labeled with input bits a and b, and output z (Mealy Machine)
…10110
…01111
…00101
a
b
z

## Slide 92: Serial Adder: State Table
a | b | Current state | z | Next state
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
(2) Write down all input and state combinations

## Slide 93: Serial Adder: State Table
(2) Write down all input and state combinations
a | b | Current state | z | Next state
0 | 0 | S0 | 0 | S0
0 | 1 | S0 | 1 | S0
1 | 0 | S0 | 1 | S0
1 | 1 | S0 | 0 | S1
0 | 0 | S1 | 1 | S0
0 | 1 | S1 | 0 | S1
1 | 0 | S1 | 0 | S1
1 | 1 | S1 | 1 | S1
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1

## Slide 94: Serial Adder: State Assignment
(3) Encode states, inputs, and outputs as bits
Two states, so 1-bit is sufficient
  A single flip-flop will encode the state
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0
1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1

## Slide 95: Serial Adder: Circuit
(4) Determine logic equations for next state and outputs
Combinational Logic Equations
  z = b + a + s + abs
  s’ = ab + bs + as + abs
Next State
Current State
Input
Output
Comb. Logic
a
b
D
Q
s
z
s'
s'
Next State
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: Practice minimizing circuit w/a Karnaugh map

## Slide 96: Sequential Logic Circuits
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Next State
Current State
Input
Output
Comb. Logic
a
b
D
Q
s
z
s'
s'
Next State
  z = b + a + s + abs
  s’ = ab + bs + as + abs
  .
  .
  .

## Slide 97: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes
  State Machines or Ad-Hoc Circuits